## Slide 1: SMART INDIA HACKATHON 2025
Problem Statement ID – SIH26007
Problem Statement Title- Safe and Efficient Operation of Mine Vehicles in Fog and Low-Visibility Conditions in Open Cast Iron Ore Mines
Theme- Smart Automation
PS Category- Hardware
Team ID- SIH26-A0H-T038
Team Name : Team Fury

## Slide 2: Fog-Adaptive Collision Avoidance System for Mining Vehicles
Team Fury
COMPLEMENTARY SENSOR FUSION
LiDAR + mmWave + Thermal sensing combine spatial, motion and thermal information for low-visibility awareness.
SYNTHETIC 2D ENVIRONMENT VIEW
Transforms heterogeneous sensor measurements into an intuitive vehicle-centered view for the driver.
LOW-COST SAFETY ARCHITECTURE
Uses affordable, commercially available components to make advanced perception more accessible for mining applications
DRIVER-CENTRIC ASSISTANCE
Provides actionable visual and audible hazard warnings instead of attempting autonomous vehicle control.
MODULAR & SCALABLE
Progressive sensor integration allows easy prototyping, testing and future enhancement.
In an open-cast iron-ore mine, haul trucks operate on: Narrow/winding haul roads, Steep gradients, Benches and ramps, Dusty environments, Heavy machinery traffic, Blind curves, Changing road conditions. Fog, especially during monsoon/early morning
During dense fog, the driver's visual horizon collapses. A truck may technically have functioning brakes, steering and lights, but the operator may detect another truck, person, obstacle or road boundary too late to react safely.
OUR PROPOSED SOLUTION
1. LiDAR-Based Environment Mapping
RPLIDAR C1 provides surrounding obstacle and environment information.
2. mmWave Radar Detection
HLK-LD2451 detects nearby moving targets and provides range/relative-motion information.
3. Thermal Sensing
MLX90640 provides thermal information to complement other sensors in poor visibility.
4. Vehicle Localization GPS provides the vehicle's position for contextual awareness.
5. Driver Assistance
Sensor information is processed and presented as a simplified synthetic 2D environment view with visual and audible hazard warnings.
ADDRESSING THE CORE PROBLEM
INNOVATION & UNIQUENESS
BACKGROUND PROBLEM
NMDC Limited is India’s largest Iron Ore producer, currently producing approximately 53 Million Tonnes Per Annum (MTPA) from its three fully mechanized mining complexes, namely BIOM-Kirandul...
In line with the National Steel Policy, NMDC has set a target of achieving 100 MT production capacity by 2030, with approximately 80 MT expected

## Slide 3: TECHNICAL APPROACH
Team fury
TECHNOLODGY USED
1. RPLIDAR C1 : 2D / 360° Environment & Obstacle Mapping
2. HLK-LD2451 : 24 GHz mmWave Radar Moving Target Detection + Relative Motion
3. MLX90640 : Thermal Camera Thermal Object Information
4. GPS MODULE : Vehicle Localization
5. ESP32-S3 :Embedded Processing & Sensor Integration
6. DISPLAY + BUZZER/LED :
Synthetic Environment View + Driver Warning
SENSOR ALIGNMENT
Common Vehicle-Centered Coordinate Frame
DATA ACQUISITION
Embedded Controller
SENSOR INPUT
LiDAR + mmWave + Thermal + GPS
FOG / LOW VISIBILITY
ENVIRONMENT & HAZARD EVALUATION
DRIVER ALERT
Display + Buzzer/LED
SYNTHETIC 2D ENVIRONMENT VIEW
DRIVER RESPONSE
System Architecture

## Slide 4
Feasibility of the Idea
Potential Challenges & Risks
Strategies to Overcome
Commercially available LiDAR, 24 GHz mmWave radar, thermal camera, GPS
Real-time local processing for immediate hazard visualization & warnings
Low-cost off-the-shelf hardware enables affordable prototyping
Modular design supports progressive sensor integration & testing
Scalable development: Prototype → Controlled Testing → Industrial Deployment
Dense fog impacts LiDAR & thermal sensing accuracy
Sensor errors risk false or missed detections
Limited range & field of view in low-cost sensors
Vehicle vibration affects sensor stability
GPS aids localization, not direct collision detection
Ruggedization & safety validation needed
for real mines
V2V/V2I communication limited by latency, range, packet loss
Use complementary sensing: radar for motion, LiDAR for range, thermal for warm objects, GPS for location
Combine distance & relative movement for risk evaluation
Cross-check overlapping sensor data to reduce false alarms
Calibrate sensor position, orientation & thresholds
Fail-safe warnings & degraded sensing indicators
on sensor faults
Prototype with affordable modules: upgrade to industrial hardware for deployment
Treat V2V/V2I as supplementary warning layer only
Progressive testing: individual sensors → integrated system → fog simulation → moving vehicles → 1/2V/V21
Team Fury
FEASIBILITY AND VIABILITY

## Slide 5
TARGET USERS & IMPACT
MINING VEHICLE OPERATORS
Earlier detection of collision hazards
Reduced dependence on visibility through windshield
Clear distance, risk and warning information
Continuous monitoring of vehicle safety conditions
Faster response to high-risk situations
Additional safety layer for existing mine safety systems
Reduced collision-related downtime
Improved operational continuity
Better safety monitoring across mining operations
Safer movement of vehicles in fog and low-visibility conditions
Improved traffic coordination
Increased production efficiency by reducing avoidable collision-related stoppages
BENEFIT ANALYSIS
SAFETY BENEFITS
Early collision warning
Dynamic safety distance based on vehicle speed and visibility
Time-to-Collision based risk assessment
Reduced risk during fog and low-visibility operation
Graduated warning from caution to critical alert
OPERATIONAL BENEFITS
Increased production efficiency
Reduced vehicle downtime caused by collision risks
Real-time local decision making
Continuous operation without dependence on cloud connectivity
Improved operator situational awareness
Supports safer vehicle movement in challenging visibility conditions
ECONOMIC & SCALABILITY BENEFITS
Low-cost prototype architecture
Uses commercially available sensors and microcontrollers
No machine-learning training infrastructure required
Modular design allows additional sensors and communication modules
Can complement existing Collision Avoidance / Proximity Detection Systems
Potentially scalable across different types of mining vehicles
MINE SAFETY TEAMS
MINE MANAGEMENT
MINING OPERATIONS
Team Fury
IMPACT AND BENEFITS

## Slide 6: RESEARCH AND REFERENCES
[1] Hrica, J. K., Bellanca, J. L., Benbourenane, I., & Stabryla, K. M. (2022). A Rapid Review of Collision Avoidance and Warning Technologies for Mining Haul Trucks. Mining, Metallurgy & Exploration, 39, 1357–1389. https://pmc.ncbi.nlm.nih.gov/articles/PMC9490765/
[2] SLAMTEC. RPLIDAR C1 Specifications. https://www.slamtec.com/en/c1/spec
[3] SLAMTEC. RPLIDAR C1 Datasheet. RPLIDAR C1 360° 2D laser scanner datasheet.
[4] Dreissig, M., Scheuble, D., Piewak, F., & Boedecker, J. (2023). Survey on LiDAR Perception in Adverse Weather Conditions. arXiv:2304.06312. https://arxiv.org/abs/2304.06312
[5] Rivera Velázquez, J. M., et al. (2022). Analysis of Thermal Imaging Performance under Extreme Foggy Conditions: Applications to Autonomous Driving. Journal of Imaging, 8(11), 306. https://www.mdpi.com/2313-433X/8/11/306
[6] Vehicle Detection and Tracking Using Thermal Cameras in Adverse Visibility Conditions. Sensors, 22(12), 4567 (2022). https://www.mdpi.com/1424-8220/22/12/4567
[7] Yang, et al. (2026). Non-Line-of-Sight Perception Method for Autonomous Haul Trucks in Open-Pit Mines Based on 4D mmWave Radar and LiDAR Fusion. Sensors, 26(14), 4615. https://www.mdpi.com/1424-8220/26/14/4615
[8] Texas Instruments. IWR6843AOPEVM Evaluation Module. https://www.ti.com/tool/IWR6843AOPEVM
Team Fury